## Slide 1: Using Lichens to Monitor Nitrogen Deposition Near Natural Gas Drilling in the Wind River Range, WY Jill A. McMurray1, Dave W. Roberts2, Mark E. Fenn1, Linda H. Geiser1, Sarah Jovan1 US Forest Service1 Montana State University2
Rapid expansion of natural gas drilling in the last decade has raised concerns about the potential ecological effects of nitrogen deposition to the Wind River Range (WRR), WY. We asked the following questions:
What is the quantity of reduced, oxidized, and total dissolved inorganic nitrogen depositing in the Wind River Range (WRR)?
What is the spatial distribution of N deposition in the WRR?
Can N concentrations from Letharia vulpina and Usnea lapponica be calibrated against annual N throughfall (TF) deposition (kg ha-1year-1) to provide an economical means to maximize future monitoring?
In the summer of 2010, nine temporary 0.378 hectare circular plots were established in the WRR just outside the Bridger Wilderness (FIA P3 Field Guide 2011). At each plot, nine passive ion exchange resin-filled collectors (IER) were installed to measure throughfall (TF) deposition (Fenn et al. 2007). In addition, lichen thalli from Letharia vulpina and Usnea lapponica were collected for elemental analysis (Geiser 2004).
Two to three plots were installed in four different drainages on the east side of the WRR in either mature Pseudotsuga menziesii or Picea engelmannii dominated forests.
After one year IER tubes were removed and two to four samples (at least 10 grams) of lichen thalli were collected from each plot for analysis.
N concentrations in lichen thalli can be used to estimate N deposition in the Wind River Range.
N deposition in the Boulder drainage is elevated (>4.0 kg ha-1year-1) with clear empirical evidence of damaged lichen thalli.
All other drainages are near background conditions which suggests a local and not a long-distance source of N pollution.
Monitoring should continue in the WRR to track changes in and increase spatial resolution of N deposition.
DIN deposition ranged from 0.78 – 4.13. The three highest DIN measurements were from the Boulder Drainage (Fig 1).
N concentrations in U. lapponica and L.vulpina ranged from 1.19 – 2.42 and 0.97- 1.56 respectively. Lichen thalli % N was highest in plots closest to oil and gas fields (Fig. 2).
Linear relationships existed between TF N and % N in lichen thalli (Fig 3-5).
Lichen samples were cleaned of debris (Geiser 2004) and sent to the University of Minnesota Research Analytical Laboratory for total ash and N analyses. Ions were extracted from IER tubes with 1 M KI (Fenn and Poth 2004) using an analysis procedure modified from Simkin et al (2004)
Within and between plot variation for both lichen N concentrations and IER TF measurements were evaluated with the coefficient of variation and standard error.
Simple linear regression was used to approximate the relationships between lichen N concentrations and TF deposition kg ha-1 year-1 for NO3-–N, NH4+–N and DIN (R Development Core Team 2011).
Study Need and Questions Asked
Methods
Analysis
Results
Conclusions
Study Area
Fenn, M.E, & Poth, M.A. (2004). Monitoring nitrogen deposition in throughfall using ion exchange resin columns: a field test in the San Bernardino Mountains. J. Environ. Qual., 33(6), 2007-2014.
Forest Inventory and Analysis Phase 3 Field Guide, version 5.1. (2011). http://www.fia.fs.fed.us/library/field-guides-methods-proc/docs/2012/field_guide_p3_5-1_sec21_10_2011.pdf
Geiser, L. (2004). Manual for Monitoring Air Quality Using Lichens on National Forests of the Pacific Northwest. USDA-Forest Service Pacific Northwest Region Technical Paper, R6-NR-AQ-TP-1-04. 126 p.
R Development Core Team (2011). R: A language and environment for statistical computing. R Foundation for Statistical Computing, Vienna, Austria. ISBN 3-900051-07-0, URL http://www.R-project.org/.
Simkin, S.M., Lewis, D.N., Weathers, K.C., Lovett, G.M., and Schwarz, K. (2004). Determination of sulfate, nitrate, and chloride in throughfall using ion-exchange resins. Water, Air, and Soil Pollut. 153, 343-354.
References
Figures
Lichens
Letharia vulpina & Usnea lapponica
Fig 1. Annual TF N deposition from four drainages in the Wind River Range. DIN refers to total dissolved inorganic N (ammonium N plus nitrate N). The red line represents background levels of N deposition in the Northern Rockies as estimated by Sverdrup et al. (2012).
DIN
r2 = 0.76
p = 0.006
Ammonium
Nitrate
Throughfall IER monitors
Green River, Pine Creek, Boulder, Big Sandy represent the three drainages in which this study took place.
Fig. 2. Log transformation of both N concentrations in U. lapponica and distance from the center of the Pinedale Anticline natural project area. curve = 7.54 – 3.38x +0.39x2. The three points in the center of the graph are not co-located,
Fig. 3-5. Simple linear regression of %N in lichen vs. throughfall (TF) dissolved inorganic N, NO3—N, and NH4+-N deposition (kgha-1year-1). Dotted lines represent 95% confidence bands.